## Slide 1: Kiln Monitoring Solutions

## Slide 2: INTRODUCTION
Fluke Process Instruments designs, manufactures and markets a complete line of infrared temperature measurement and profiling solutions for industrial, maintenance, and quality control applications. Distributed worldwide under the Raytek, Ircon, and Datapaq brands, the products reflect the combined experience of over 150 years in manufacturing the world’s finest temperature measurement tools and devices.
Notes: Let me give you brief introduction about fluke process :
Fluke process instruments established in 1948 is one of the leading Manufacturer of Noncontact infrared industrial temperature measurement instruments in the world.
We are Raytek, Ircon, and Datapaq. Together, we are Fluke Process Instrument
Our robust monitoring solutions include pyrometers, fixed thermal imaging cameras, and infrared linescanners, and are designed for your harshest environments.
we are the temperature technology leader many of the industry firsts pioneers , Every year we are developing new technologies and market innovations and the brands of choice for the harshest, high-temperature industrial environments in manufacturing.
World class temperature measurement solutions in fluke process
Temperature Uniformity Ensure materials such as metals, glass, plastics, and more maintain material viscosity by easily measuring temperature uniformity. Industry Compliance Ensure your compliance with industry-specific regulations and specifications such as CQi-9 and AMS2750 standard
Hot Spot Detection Quickly detect hot spots and other potential problems, allowing you to avoid costly machinery damage and unscheduled downtime Optimize Performance Save time on furnace setup, thermal surveys, process optimizations and more.
Real-Time Data Observe your process and analyze data in real-time with customizable areas of interest; independent, continuous, or intermittent evaluation; and more.
And also under the Fluke process instruments – Raytek ,Ircon,Datapaq brands products combined experience of over 150 years in manufacturing of world finest temperature tools and devices.
Fluke process Instruments have two Categories one is Monitoring and another one is Profiling
Raytek & Ircon – Monitoring
Datapaq is a profiling ---
Profiling means Temperature data is measured continuously using thermocouples connected directly to the product(s) at different locations as it travels through the oven or furnace.
What is Thermal Profiling?
Temperature profiling is the term used to describe the process of recording and interpreting the temperatures of products and/or air through a conveyorized heat-treating process. Temperature data is measured continuously using thermocouples connected directly to the product(s) at different locations as it travels through the oven or furnace.
Raytek designs manufacture, markets, and services a complete line of infrared, noncontact temperature measurement instruments for continuous temperature monitoring induction Furnace, process control, maintenance, Power industries, Safety preventions applications. FPI-Raytek is represented globally by their worldwide network of Distributors.
A triad of the top performing, most rugged and dependable noncontact temperature measurement and profiling equipment made – a complete line of infrared sensors, line scanners, thermal imagers and profiling systems for use in today's most demanding environments.
Individually, we have earned the respect of manufacturing’s most valued names. Together, we are the temperature technology leader – pioneers of many industry firsts, market innovations and new technologies, and the brands of choice for the harshest, high-temperature industrial environments in manufacturing.
Precisely, accurately, and with the greatest of detail, all to ensure our customers’ promise of quality is delivered.
With over a century of combined experience in developing innovative products that improve product quality and reduce waste, our team is committed to achieving new advancements that will benefit our customers.

## Slide 3: Major Applications
Kiln Shell Temperature Monitoring
Burning Zone Pyrometer
Clinker Temperature at Cooler End

## Slide 4: Kiln Shell Temperature Monitoring
CS400 System
Temperature Monitoring, Control and Analysis for Rotating Kilns

## Slide 5: Rotatory Kiln Basics
Material enters the cold end and is converted as it approaches the burning zone.
End product, clinker, exits the hot end of the kiln for further processing.
The kiln is made from steel lined with ceramic refractory material to protect the steel from the heat of the burner.
Checking the status of the refractory is critical to maintaining kiln performance and preventing catastrophic breakdown.
Feed In
Tire
Refractory Lining
Steel Shell
Burner Pipe
Flame
Clinker to Cooler

## Slide 6: Benefits
Downtime is very costly, catastrophic failure even more so!
Detect hotspots due to refractory loss, damage or wear
Extend operational life of kiln and refractory
Optimize and manage kiln maintenance
Completely integrated monitoring of key kiln parameters
Detect abnormal operating conditions, such as faulty flame position & shape
Other applications on lime kilns but also in metals and chemical processing
FPI already has more then 500 installations worldwide with successful CS100/CS200/CS210 products!
Running from more then 20 years.

## Slide 7: Overview
Connection Box
Housing &
Scanner
Control Room
Housing &
Scanner
Connection Box
Kiln
Trigger Bar
Position Indicator
Single fiber- optic cable
Monitor the Burning Zone
Burning Pyrometer/imager
Compensate for Shadows
Shadow Pyrometers
Control up to 48 Cooler Fans
Wago I/O module
Standard Computer + CS Software
Connection Box
Measure the Tire Slips
Tire Slip Monitoring
Optional remote clients
Network Switch from 2nd NIC

## Slide 8: About Line Scanner
Rotating motor scans target through window
1024 points are collected within the 90° field-of-view
“One brick” resolution hot spot detection of 510:1
Built-in heater & internal temperature compensation
PC independent alarm relay is activated when temperature out-of-range occurs
Maximal 4 scanners supported (long kilns, obstacles)
Detector
Lens/filter
Mirror
Brushless motor
Ambient black body

## Slide 9: Protective Housing
Protects Linescanner, high quality rugged Stainless-Steel housing
Air purge keeps scanner lens free of contamination
3D-adjustable mounting base

## Slide 10: Position Indicator
Synchronizes Thermal Imaging & Kiln Rotation
Resistant to high temperatures (230°C/466°F)

## Slide 11: System Connection Box
Field mounted cabinet
Modular design for field additions or replacements
Converts Ethernet to fiber-optic communications
Serial/Ethernet converter to support accessories
Optional heater for ambient temperatures down to -20°C/-4°F

## Slide 12: Fan Control – Hardware Outputs
Assists in preventing kiln shell deformation with active cooling via multiple fans
Software controlled turn on/off for up to 48 fans
Digital output module type:
  16 channels per card
  2 channels per card, relay NO
Additional cards can be added later
Digital input
Analog output

## Slide 13: Fiber-Optic Communication Box
Field mounted cabinet
Modular design for field additions or replacements
Converts Ethernet to fiber-optic communications
Serial/Ethernet converter to support accessories
Optional heater for ambient temperatures down to -20°C/-4°F

## Slide 14: Accessories
Hardware:
  Tire Slip Monitoring TSM
  Burning Zone Monitoring
  Shadow Monitoring
  Fan Control
Software
  Refractory Management
  3D Real Time View

## Slide 15: Tire Slip Monitoring
Monitor “creep” of the kiln and prevents mechanical damage to refractory
Measures the offset in rotation between the kiln shell and each tire
Delivery: TSM controller and 3 position indicators
Maximum 6 tires in total
TSM data viewable directly from CS software screens with multiple choices for data presentation

## Slide 16: Shadow Monitoring
Monitors shadows created by kiln tires and other immoveable objects
Thermal data is incorporated with linescanner data into one seamless thermogram
Standard package consists of: IR sensor, air purge, adjustable mounting bracket, connection box
Multi-drop up to several sensors to monitor multiple shadows

## Slide 17: CS400 – New Launch : Nov 2021

## Slide 18: Software
CS400 Standard and Advanced
CS400 Standard
Mutliple Scanner
Support
(Standard)
3D Real
Time View
(Standard)
CS400 Advanced includes:
  Multiple kiln connectivity
    Monitor more than one kiln at the same facility using a single license – Reduce system cost.
  Refractory Management (RFM)
    refractory management system – calculated using refractory properties and external temperature data.
  Polar chart (Coating thickness)
    Multiple polar chart visualizations options –feature allowing operator to understand coating thickness in every area of the kiln.
  Envelope profile
    Visualization showing min/max temperature along kiln length – Effective tool for operator hand over.

## Slide 19: Software
Main Screen
Temperature thermogram
Temperature line graph
One screen shows temperature data and all needed information to monitor kiln and CS210 system condition.
Refractory zones
Alarm status
Polar chart
Area of interest

## Slide 20: CS400 Key features and improvements
Coating, thickness and brick thickens – Polar chart
Envelope Profile over the complete kiln including alarm functionality
Multiple Kiln Support
No more SQL Database like in CS210 and History can be stored on network.
Ability of Short Term, Mid Term (New) and Long Term (more flexible)
Imager Support (TV40) (Note : Additional Hardware is Required)
Different Pyrometer support (using all FPI Pyrometers for BZ, SM – Mi3, T4.0, EN, TV40) (Additional Hardware Kit Required)
Analog and Digital I/O (Wago)
BZ support EN video functionality (Note : Additional Hardware is Required)
Free scalable AOI (Areas, line, slice) including temperature trend analyze
Virtual 3D walk through entire kiln
3D view per defined kiln zone
Easy software configuration for the Scanner kiln position.
Support OPC DA and Latest industrial protocol OPC UA coming later Q3.
Flexible Image sizing and Orientation of rotation free configurable
Existing Customer can Upgrade to CS400 : Optional

## Slide 21: Modularisation
CS Scanner kits
CS401-MP150-KIT
CS402-MP150-KIT-2
CS403-MP150-KIT-3
CS404-MP150-KIT-4
Basic HW kit
CS400-HW-KIT-BASIC
Contains:
Fiberoptic converter housing
Position sensor and junction box
Software options
CS400-SW-STD
CS400-SW-ADV
Upgrade from STD to ADV
CS400-SW-ADV-UPG
Upgrade from CS210 to CS400 STD
CS400-SW-CS210-UPG
Accessory kits
A-CS-BZ-EN-KIT-485 Burning zone monitoring
A-CS-SM-KIT-485 Shadow monitoring
A-CS-TSM-KIT-485 Tire slip monitoring (used to be live ring migration)
A-CS-CNV-ETH485 Serial ethernet converter

## Slide 22: Kiln Monitoring Solutions
Thank you for your attention!
For more information, visit www.flukeprocessinstruments.com